## Slide 1
Problem Formulation
David Blum
Postdoctoral Fellow
Building Technology and Urban Systems Division
Lawrence Berkeley National laboratory
Office: 90-3145
Phone: +1 (510) 486-4741
Email: dhblum@lbl.gov

## Slide 2
MPCPy
Open-source software framework for MPC in buildings
Features
Exogenous data collection
Building system emulation or
data collection
Grey-box parameter estimation
Control optimization
Non-MPC-expert usability
Design
Python scripting
Utilize support software
Extensible
Open-source
Tool
[1] Blum, D. H. and M. Wetter “MPCPy: An Open-Source Software Platform for Model Predictive Control in Buildings.” Proceedings of the 15th Conference of International Building Performance Simulation, Aug 7 – 9, 2017. San Francisco, CA.
https://github.com/lbl-srg/MPCPy

## Slide 3
General Process with MPC Platform
JModelica
MPCPy
User
solution information
model.mop
Optimica
direct collocation &
derivatives
casADi
model.mo
case information
NLP solve
IPOPT
Optimal
Control
Law
Tool

## Slide 4
Coefficient Estimation
JModelica
MPCPy
User
measurement
weather
Internal load
model.mop
Optimica
direct collocation &
derivatives
casADi
model.mo
coefficient
information
NLP solve
IPOPT
Optimal
Control
Law
Tool

## Slide 5
Control Optimization
JModelica
MPCPy
User
weather
internal load
prices
constraint val
model.mop
Optimica
direct collocation &
derivatives
casADi
model.mo
objective
constraint def
NLP solve
IPOPT
Optimal
Control
Law
Tool

## Slide 6
package Example
model House
parameter Real R “Resistance”;
parameter Real C “Capacitance”;
parameter Real COP “Coefficient of Performance”;
input Real T_amb “Ambient Temperature”;
input Real Q_hvac “HVAC heating power”;
Real T “Indoor Air Temperature”;
Real P “HVAC Electrical Power”;
equation
C*der(T) = (T_amb-T)/R + Q_hvac;
P = Q_hvac/COP;
end MPC;
model MPC_initialize
House mpc_model(R = r, C = c, COP = cop);
input Real T_amb = mpc_model.T_amb;
input Real Q_hvac = mpc_model.Q_hvac;
input Real price;
Real J(start = 0);
equation
der(J) = mpc_model.P*price;
end MPC_init;
optimization MPC_optimize(objective=J(finalTime))
extends MPC_initialize;
input Real T_lte_constraint;
constraints
mpc_model.T < T_lte_constraint;
end MPC_optimize;
end Example;
Original Model
Initialization Model
instantiate original model
add additional inputs
add objective variable
define objective equation
(could include soft constraints)
use initialization model
define constraints
Optimization Definition
add constraint inputs
add necessary inputs
Tool
From [Blum and Wetter 2017]

## Slide 7
Detailed model for building emulation
Test building design
Detailed building model in Modelica
Example
From [Blum and Wetter 2017]

## Slide 8
“Grey-box” three-zone RC envelope model for MPC
Example
From [Blum and Wetter 2017]

## Slide 9
Example

## Slide 10
Example
From [Blum and Wetter 2017]

## Slide 11
Thank you!
David Blum
Postdoctoral Fellow
Building Technology and Urban Systems Division
Lawrence Berkeley National laboratory
Office: 90-3145
Phone: +1 (510) 486-4741
Email: dhblum@lbl.gov

## Slide 12
MPCPy
Open-source software framework for MPC in buildings
LBNL Work
Blum, D. H. and M. Wetter “MPCPy: An Open-Source Software Platform for Model Predictive Control in Buildings.” Proceedings of the 15th Conference of International Building Performance Simulation, Aug 7 – 9, 2017. San Francisco, CA, Accepted.
https://github.com/lbl-srg/MPCPy

## Slide 13
MPCPy
Open-source software framework for MPC in buildings
LBNL Work
Blum, D. H. and M. Wetter “MPCPy: An Open-Source Software Platform for Model Predictive Control in Buildings.” Proceedings of the 15th Conference of International Building Performance Simulation, Aug 7 – 9, 2017. San Francisco, CA, Accepted.
https://github.com/lbl-srg/MPCPy

## Slide 14
MPCPy
Open-source software framework for MPC in buildings
LBNL Work
Blum, D. H. and M. Wetter “MPCPy: An Open-Source Software Platform for Model Predictive Control in Buildings.” Proceedings of the 15th Conference of International Building Performance Simulation, Aug 7 – 9, 2017. San Francisco, CA, Accepted.
https://github.com/lbl-srg/MPCPy

## Slide 15
MPCPy
Open-source software framework for MPC in buildings
LBNL Work
Blum, D. H. and M. Wetter “MPCPy: An Open-Source Software Platform for Model Predictive Control in Buildings.” Proceedings of the 15th Conference of International Building Performance Simulation, Aug 7 – 9, 2017. San Francisco, CA, Accepted.
https://github.com/lbl-srg/MPCPy